## Slide 1
ECE4078 Intelligent robotics
Lab 4-1: Semi-Auto Navigation
AI art generated by https://www.craiyon.com/
(prompt: “a penguin robot shopping for fruits and vegetables in a supermarket”)

## Slide 2
Week | Objectives | Milestones
1: M1-1 | Introduction and setup | 
2: M2-1 | Calibration, ARUCO markers | M1 due
3: M2-2 | SLAM | 
4: M2-3 | SLAM | 
5: M3-1 | Object recognition & localisation | M2 due
6: M3-2 | Object recognition & localisation | 
7: M4-1 | Navigation & Planning | M3 due
8: M4-2 | Navigation & Planning | 
9: M5 | Integration & Improvement | M4 due
10: Final | Trial run of final demo | M5 due
11: Final | Improving your final demo | 
12: Final | Final demo | Final demo
ECE4078 Intelligent robotics
*

## Slide 3
M4: Navigation and Planning
M4 focuses on navigation and planning
PenguinPi now knows where things are and needs to plan its way around the supermarket and get fruits&vegs on its shopping list
Your task will be to semi OR fully autonomously navigate and path plan around the arena to targets in a specified order
The arena will always contain:
10 ArUco markers
10 Fruits&Vegs
Groundtruth maps are given for M4 ONLY (practice map in repo)
You will be given a shopping list that contains 5 targets in the order for the robot to navigate to
The 5 targets will be unique, the 5 obstacles may contain duplicates of other types
To “pick up” a target you must stop the robot for 2 seconds (doesn’t need to be exact) whilst being within 0.5m of the target

## Slide 4
M4: Navigation and Planning
There are 3 levels of difficulties which you can choose to complete the task in:
Level 1: Semi-auto navigation + known map
- You will be provided with the location of all objects within the arena
- You may control the robot by inputting “waypoints” for the robot to travel to
- You can NOT teleoperate the robot (you can’t use keyboard inputs to drive the robot like in M2/M3)
Level 2: Fully autonomous navigation + known map
- You will be provided with the location of all objects within the arena
- You are only allowed to enter a single command to start the robot
- The robot should autonomously complete the task without human intervention
Level 3: Fully autonomous navigation + partially known map
- You will be provided with the location of all objects EXCEPT the 5 obstacle fruits&vegs
- These unknown obstacles are strategically placed such that there is a high probability that your generated path will intersect them. You will have to use your M3 to detect the obstacle fruit
-You are only allowed to enter a single command to start the robot
-The robot should autonomously complete the task without human intervention

## Slide 5
M4: semi-auto waypoint nav (wk7)
Level 1: semi-auto navigation with manually given waypoints
You can do this by modifying the skeleton code “auto_fruit_search.py” provided to you
The skeleton code works by:
  1: Receiving a waypoint that are inputted by the user
  2: Navigate the robot to the waypoint based on the estimated time it needs to turn and drive (implemented by you)
  3: Repeat step 1&2 until task is complete
  There are 3 things you need to change
  1: Calculate the time required to turn (in drive_to_point function)
  2: Calculate the time required to drive forward (in drive_to_point function)
  3: Calculate the new pose of the robot (in get_robot_pose function)

## Slide 6
Recommendations (optional)
- Visual localisation
The skeleton code does not use any visual features (ArUco markers) in estimating its current pose, relying solely on dynamics to estimate the robot’s current position in the arena.
It is highly recommended that you implement a more robust localisation system that uses the ArUco markers like you did in M2. You do not have to generate / update the markers as the true location of the 10 markers is given to you at the start
- Controller based waypoint navigation
By default, the skeleton code travels to waypoints based on an initial time estimate.
A small error in the initial rotation can cause a large error in the final position if traveling long distances
You can improve this by using a proportional controller to gently steer the robot so that it is always moving towards the waypoint given visual feedback on the robot’s pose
- Better GUI
Manually inputting coordinates by hand is slow and prone to error, an interactive map to click on to create new waypoints would be more efficient
It is also difficult to tell if the robot is within 0.5m of a target or if the robot’s pose estimation has drifted without any graphical feedback, therefore this should be included in the GUI as well

## Slide 7
M4: auto nav (wk8)
Level 2:
auto navigation with known map (waypoints produced by your path planner)
Level 3:
auto nav with partially known map (use M3 to detect obstacles and replan once an obstacle is seen)
You can do this by modifying “auto_fruit_search.py” or write your own scripts
Will talk about these more next week

## Slide 8
M4: Evaluation
Live demo marking in wk9 using new arena
Each of the 3 levels have different marks associated
Level 1: (Total marks: 60pt)
For each successful navigation in order +12pts
Level 2: (Total marks: 20pt)
You get the Lv1 60pt if you can achieve a qualified run in Lv2
For each successful navigation in order +4pts
Level 3: (Total marks: 20pt)
You get the Lv1+Lv2 80pt if you can achieve a qualified run in Lv3
For each successful navigation in order +4pts
You will receive penalties if:
Robot collides with marker/object (-2pt)
Robot goes out of arena boundaries (-5pt)
Max 3 penalties allowed: third time a penalty happens that run is disqualified and gets 0pt
Will talk more about evaluation rules next week

## Slide 9
M3: Marking
Detector performance:
Classification performance of your trained YOLO on a set of 10 testing images. You will need to pass the testing images into your model using detector.py (inside YOLO folder)
detector_score = 2 x NumberOfCorrectPredictions (0 ≤ detector_score ≤ 20)
Target map performance:
Driving your robot around the arena to generate slam.txt and targets.txt, then mapping_eval.py will be used to calculate the estimation error.
mapping_eval.py takes your slam.txt to get the alignments for best SLAM, then the target positions from targets.txt are re-aligned accordingly. The Euclidean distance between each target and its closest estimation is recorded as target_score.
target_score[object] = (1 - estimation_error[object]) / (1-0.025) x 8
target_est_score = sum(target_score) – 5 x NumberOfCollisions 0 ≤ target_est_score ≤ 80
M3_score = detector_score + target_est_score 0 ≤ M3_score ≤ 100

## Slide 10
M3: Marking
Before the lab:
Submit your code (link to BestYoLo.pt if too big)
Before marking:
Check the marking schedule
Download the detector testing image set of your lab
During live demo:
Download and unzip submission
Demonstrate detector performance on marking set (show visualisation of bounding box and label)
Run operate.py to map the arena (run SLAM with ENTER and save pose+observation with “n”)
Generate targets.txt after a run with TargetPoseEst.py (save slam.txt and targets.txt with run ID)
Submit slam.txt & targets.txt