## Slide 1
ECE4078 Intelligent robotics
Lab 2-3: Evaluation and Marking
AI art generated by https://www.craiyon.com/
(prompt: “a penguin robot shopping for fruits and vegetables in a supermarket”)

## Slide 2
Week | Objectives | Milestones
1: M1-1 | Introduction and setup | 
2: M2-1 | Calibration, ARUCO markers | M1 due
3: M2-2 | SLAM | 
4: M2-3 | SLAM | 
5: M3-1 | Object recognition & localisation | M2 due
6: M3-2 | Object recognition & localisation | 
7: M4-1 | Navigation & Planning | M3 due
8: M4-2 | Navigation & Planning | 
9: M5 | Integration & Improvement | M4 due
10: Final | Trial run of final demo | M5 due
11: Final | Improving your final demo | 
12: Final | Final demo | Final demo
ECE4078 Intelligent robotics
*

## Slide 3
Recap
M2: SLAM
Your task is to estimate the position of all 10 ARUCO markers within the 3mx3m arena
Task 1: Wheel calibration (Week 2)
- Objective is to calculate the wheel radius and the distance between both wheels
Task 2: Camera calibration (Week 2)
- Objective is to calculate the intrinsic parameters of the camera
Task 3: SLAM (Week 3 & 4)
- Estimate the position of markers in the environment using an Extended Kalman filter (EKF)
- Two main files to modify:
- “slam/ekf.py”: “predict()” and “update()” functions
- “slam/robot.py”: “derivative_drive()” and “covariance_drive()” functions
- Your solution should automatically generate “lab_output/slam.txt” for evaluation

## Slide 4
M2 – Evaluation
Your received mark for this milestone will depend on the output of the “SLAM_eval.py” script which compares the true marker positions and your estimated marker position in “lab_output/slam.txt”
“SLAM_eval.py” will calculate an aligned RMSE to evaluate how well your solution worked at estimating the position of ArUco markers
Total of 100 points:
slam_score = [(0.12 – Aligned_RMSE)/(0.12-0.02)] x 80
Total M2 mark = slam_score + (Number of Found Markers x 2) – (Number of Collided Markers x 5)
0 ≤ slam_score ≤ 80
0 ≤ M2 total score ≤ 100
Max allowed number of collision in a run is 3 times (the 4th time you’ll be asked to terminate that run)
You’ll need to make a visible effort to try and location all 10 markers

## Slide 5
M2 – Marking
Submit your M2 implementation before the Week 5 lab for live demo marking
Step 1: (BEFORE submitting your solution)
Submit a zipped folder containing:
Necessary files to run your solution (no need to include your Python venv)
A text file of commands for easy copying and pasting (optional)
Step 2: (BEFORE the demonstrator comes to mark you)
- Close all folders / applications / windows in your ubuntu environment
- Log into Moodle and navigate to the M2 submission box
- Have an empty folder called “LiveDemo” in the home directory ( ~/LiveDemo/ )

## Slide 6
M2 – Marking
Step 3: (DURING the marking period)
- Come to the marking arena ONLY when it’s your group’s turn
- Download your submission from Moodle into the LiveDemo folder and extract the contents
- Activate your Python venv
- Connect to your robot
- Navigate into the unzipped submission
- When the demonstrator says it’s fine to start you may run your SLAM demo
- You can run SLAM several times and submit all the maps generated
- When complete, submit your generated maps (lab_output/slam.txt) to Moodle
You have a strict time limit of 15min in total for Step 3 (live demo marking), including the download, re-setting arena layout / robot location if needed in between runs, and map submission.
Read M2_marking_instructions.md carefully and get familiar with the marking steps